## Slide 1
RESEARCH PROJECT REPORT
A Cycle-Accurate Simulator for H3
Hybrid HBM + High Bandwidth Flash memory for long-context LLM inference
44
new files written
10,600
lines of code
197
automated checks passing
2
simulators integrated

## Slide 2
01
Why this project exists
The problem, and what the paper does about it
2

## Slide 3
BACKGROUND
Long context is a capacity problem
H3 cycle-accurate memory simulator
3
Llama 3.1 405B at 10M tokens needs about 2.5 TB per GPU for the KV cache
HBM tops out near 192 GB per GPU, so the data simply does not fit
H3 adds a second memory tier: High Bandwidth Flash
Same bandwidth as HBM at 8 TB/s, but 16x the capacity at 3 TB
Reads take 20 microseconds, against 19.5 nanoseconds for HBM
The whole design rests on hiding that delay by fetching data early
IN PLAIN WORDS
Flash memory is large and cheap but slow to start reading. H3 bets that because LLM inference is predictable, data can be fetched before it is needed. Our job was to build a simulator that can check whether that bet holds.

## Slide 4
POSITIONING
The paper's method, and ours
H3 cycle-accurate memory simulator
4
THE PAPER
Analytical model, its Section IV-A
Adds up compute, transfer and communication time
Does not simulate individual memory requests
Fast to run, but assumes the buffer works
WHAT WE BUILT
Cycle-accurate simulation
Every memory request modelled individually
Bank conflicts, queueing, open pages all included
Slower, but can test the assumption
IN PLAIN WORDS
Our simulator is more detailed than the published method, not less. The paper calculates how much H3 would help if the latency-hiding buffer works. Ours can measure whether it actually does.

## Slide 5
02
How it was built
Tools, environment, and integration
5

## Slide 6
TOOL CHOICE
What we chose, and why
H3 cycle-accurate memory simulator
6
CHOSEN
Accel-Sim / GPGPU-Sim 4.x
The standard academic GPU simulator
Ramulator 2.1
New memory types defined in Python, not C++
Docker, linux/amd64
Tools need CUDA 12.8 on Linux
WHY IT MATTERS
Both are published and peer-reviewed
Results are comparable with other work
Trace-driven, so no GPU needed to run
The whole thing runs on a laptop
Nothing written from scratch
IN PLAIN WORDS
We did not build a GPU simulator ourselves. We took two established simulators, joined them, and added only the parts that describe H3 specifically.

## Slide 7
ENVIRONMENT
Setting up the build
H3 cycle-accurate memory simulator
7
Read the repository's own config files rather than guessing versions
The devcontainer file and README both pointed to CUDA 12.8 on Ubuntu 24.04
Wrote Dockerfile.h3sim and docker-compose.yml from those findings
Found three dependencies the official instructions leave out
python3-dev, needed because the build calls pybind11
libzstd-dev, needed for compressed traces
cmake itself, missing from the documented package list
IN PLAIN WORDS
Rather than assuming which software was needed, we read the project's own configuration. That is how we found three missing packages that would otherwise have caused confusing failures partway through a 30 minute build.

## Slide 8
INTEGRATION
Linking the two simulators
H3 cycle-accurate memory simulator
8
GPGPU-Sim's memory class has no plug-in point for a new memory type
But it already had a switch for a second, simpler memory model
-gpgpu_simple_dram_model, at gpu-sim.cc line 243
DECISION: copy that exact pattern rather than invent a new one
-gpgpu_memory_backend 2 now selects H3; the other two paths are untouched
DECISION: deliver the change as a patch file, not by editing the simulator
310 lines across 5 files, applied and reverted by one script
IN PLAIN WORDS
We followed a pattern the simulator already used. This keeps the change small, easy to review, and reversible. With H3 switched off, the original simulator behaves exactly as before.

## Slide 9
ARCHITECTURE
How a memory request flows
H3 cycle-accurate memory simulator
9
GPU cores
Accel-Sim / GPGPU-Sim
L2 cache
memory partition x40
H3 address router
HBM or flash?
HBM3e
192 GB - 19.5 ns
Latency hiding buffer
40 MB SRAM - 2 ns
HBF flash
3 TB - 20 microseconds
Prefetch scheduler feeds the buffer ahead of time
IN PLAIN WORDS
A request leaves the GPU, passes through cache, then the router decides whether it belongs in fast HBM or slow flash. Flash requests go through the buffer, which usually already has the data because the scheduler fetched it in advance.

## Slide 10
03
The components we wrote
Four pieces, and the decisions behind them
10

## Slide 11
FLASH MODEL
Building the flash memory model
H3 cycle-accurate memory simulator
11
Found that Ramulator's memory models are GENERATED from Python, not hand-written
The C++ files carry an AUTO-GENERATED, DO NOT EDIT banner
DECISION: write the model as Python, at ramulator_hbf/hbf.py
Hand-written C++ would have been erased on the next build
Key insight: a flash page read has the same two-step shape as DRAM
Step 1 reads the flash array into a buffer, and takes 20 microseconds
Step 2 moves data from that buffer onto the bus, and is fast
IN PLAIN WORDS
Flash and DRAM look very different, but the sequence of operations is similar enough that we could reuse Ramulator's existing machinery rather than writing a new memory simulator from nothing.

## Slide 12
FLASH MODEL
Decisions inside the flash model
H3 cycle-accurate memory simulator
12
64
planes per channel
not arbitrary, see below
16 KB
flash page size
one row in the model
4 TB
address space
3 TB actually exposed
0
refresh operations
declared but never used
To keep 32 GB/s flowing through a 20 microsecond delay, 40 pages must be in flight at once. 64 planes gives 1.6x headroom.
Capacity is rounded up to a power of two because Ramulator's address decoder cannot handle 3 TB directly. The router exposes exactly 3 TB.
IN PLAIN WORDS
Every one of these is a deliberate compromise, written down in docs/hbf_model.md together with what would need to change for a more accurate flash model.

## Slide 13
COMPONENTS
The router and the buffer
H3 cycle-accurate memory simulator
13
ADDRESS ROUTER
Decides HBM or flash for every request
Weights and shared cache go to flash, never written
Generated cache and activations go to HBM
Enforces that flash is read-only
Adds the 25 ns die-to-die crossing cost
LATENCY HIDING BUFFER
Fetches data before the GPU asks for it
Two halves: read one, fill the other
FINDING: the paper's Equation 1 is a balance condition
Draining a half and filling it both take 20 microseconds
DECISION: modelled as a streaming buffer
IN PLAIN WORDS
The router is also a correctness check: if a write ever reaches the read-only flash region, a counter becomes non-zero and we know data was placed in the wrong memory. The buffer streams because one layer's weights are 870 MB against a 40 MB buffer.

## Slide 14
COMPONENTS
The prefetch scheduler
H3 cycle-accurate memory simulator
14
Decides WHEN to start fetching each piece of data
Works because LLM inference is completely predictable
Every tensor read is known before the first token is generated
There is nothing to guess, only to schedule
VALIDATION: our arithmetic independently reproduces the published model
405.9 billion parameters, matching the 405B in the model name
35% and 84% cache occupancy, matching the paper's figures exactly
IN PLAIN WORDS
This is the strongest evidence that our model of the workload is right. We never downloaded the model. We computed tensor sizes from the published architecture and arrived at the same numbers the paper reports.

## Slide 15
FINDING
A discrepancy worth reporting
H3 cycle-accurate memory simulator
15
WHAT THE MODEL USES
Llama 3.1 405B officially uses grouped-query attention
8 key-value heads
That gives a cache occupancy of about 2 percent
Nowhere near the paper's 35 percent
WHAT MATCHES THE PAPER
Full attention with 128 heads at FP16
Gives exactly 35 and 84 percent
DECISION: default to the paper's values
Switching to the official config is one line
IN PLAIN WORDS
This matters because with the official configuration the cache is 16 times smaller, and the case for a 3 TB flash tier weakens considerably. We could not resolve it from the paper, so we documented both rather than choosing silently.

## Slide 16
04
Testing and results
What works, what does not, and what it cost
16

## Slide 17
TESTING
How we tested it
H3 cycle-accurate memory simulator
17
APPROACH
197 automated checks in 5 test programs
DECISION: H3 code depends on neither simulator
So tests run in seconds, not after a 30 minute build
A trace checker validates input before the simulator sees it
WHAT IS CHECKED
A buffer hit must generate NO flash traffic
Data in transit must never be reported as ready
Per-GPU settings must be divided across partitions
Several tests exist because they caught a real bug
IN PLAIN WORDS
Keeping our components independent of the large simulators means a mistake shows up in seconds rather than after a long build. Each test that guards a past bug is named for the problem it prevents.

## Slide 18
RESULTS
Bugs the detailed model exposed
H3 cycle-accurate memory simulator
18
26x
flash traffic overstated
requests sent before the buffer was asked
4,273
false buffer hits
data in transit marked as arrived
40x
GPU speed overstated
per-GPU settings applied per partition
All three were invisible to the fast model, which happily returned a plausible number. The detailed model refused, and threw an error instead.
All three are fixed, and each now has a test that prevents it returning.
IN PLAIN WORDS
This is the strongest argument for building the cycle-accurate version at all. Two models that disagree are how you discover that one of them is wrong.

## Slide 19
RESULTS
What the simulator measures today
H3 cycle-accurate memory simulator
19
3x
more work done
buffer on versus off
0.74
buffer hit rate
measured, not assumed
6,074 ns
average latency
matches prediction
0
correctness errors
all three counters clean
Same trace, same settings, the only difference is the buffer being switched on.
Predicted latency from hit rate was 5,829 ns against 6,074 ns measured, so hits, misses and timing now tell one consistent story.
IN PLAIN WORDS
The 3x figure is measured rather than assumed. Both sides of that comparison are identical apart from the buffer, which is what makes it a fair test.

## Slide 20
STATUS
Where the project stands
H3 cycle-accurate memory simulator
20
WORKING
Full pipeline runs end to end
200,000 cycles, clean exit, both memory models working
WORKING
Flash model, router, buffer, scheduler
All four components built, tested and integrated
WORKING
Published to GitHub with both simulators as submodules
Reproducible on another machine with one clone command
PARTIAL
Power modelling
First-order only; command-level counts not yet wired through
PLANNED
Real Llama traces
Needs a machine with NVIDIA A100 or H100 GPUs
NOT DONE
The paper's 2.69x throughput-per-watt figure
Would need the analytical model, which we chose not to build
IN PLAIN WORDS
The simulator is built and validated. Being correct and being complete are two different things, and only the first is true today.

## Slide 21
LIMITS
Honest limits of the current results
H3 cycle-accurate memory simulator
21
The test workload is a stand-in, not a real LLM trace
It has no computation between memory accesses, which is the worst case
The run is too short to reach steady state
64 microseconds of simulated time is about three buffer refills
The HBM-only comparison currently assumes a GPU with 3 TB of HBM
No such GPU exists; the paper compares at equal GPU count instead
These limits are written into the project README, not hidden
IN PLAIN WORDS
We would rather state clearly what the setup cannot yet support than quote a number it cannot justify. Each limit has a known fix, listed in the next steps.

## Slide 22
VALUE
What this simulator adds
H3 cycle-accurate memory simulator
22
THE PAPER ESTABLISHES
That H3 is worth building
Sizes the buffer with an equation
And assumes it works from there
OURS CAN EXAMINE
Whether the buffer really hides the delay
Hit rate, stall length, late prefetches
How sensitive the design is to flash latency
Where the cliff is with too few flash planes
Whether prefetch and demand reads fight for banks
IN PLAIN WORDS
This is where the contribution lies. The paper argues H3 should work. This simulator can test whether the mechanism that makes it work behaves as expected under realistic conditions.

## Slide 23
NEXT
Suggested next steps
H3 cycle-accurate memory simulator
23
1. Fix the comparison point before generating any traces
The paper compares at equal GPU count, where H3 allows a 2.6x larger batch
This costs nothing and decides which traces are worth generating
2. Generate real Llama traces on a machine with A100 or H100 GPUs
Requirements written up in docs/large_machine_requirements.md
3. Complete the power model if the throughput-per-watt claim is needed
4. Run the sensitivity sweeps the analytical model cannot reach
IN PLAIN WORDS
Step 1 should come first because it is free and it determines everything after it. Generating traces costs days and terabytes, so it is worth being certain about the experiment before starting.